DASH7 Implementation

###### Introduction

This implementation does a part of the DASH7 mode 2 stack specification using ChibiOS. It was developed as a project from the college Telecom Paristech.
The project was a continuation from the WaDeD project (also from Telecom Paristech) developed by Hubert Lefèvre, Patrick Lambein, Pedro Terra Delboni, and Sasha Delanoue.
Samuel Tardieu was the instructor for both projects and Alexis Polti was also instructor for the WaDeD project.

The result of this project is a library that can be used to create applications that are compatible with the DASH7 standard.

For a better understanding of this document please have in hand the code (which is commented to help the understanding) and the DASH7 specification
###### dash7/phy.h

Here are the functions that will handle the physical layer (PHY). Here the PHY is not completely separated from the data layer (DATA) because information from the DATA was needed to make better use of the transceiver.

The PHY implementation work with a procedure targeted architecture. This was done so multiple threads may each have its own procedure and share the transceiver.
When a procedure is started, every command within it will not be interrupted by another thread procedure in order to guarantee that during this period the configuration of the transceiver remains unchanged. In the procedure the user is allowed to send and receive DASH7 frames.
It is important to notice that in DASH7 there is a difference from frame and packet where frame are the payloads with its headers and footers and packet is what is sent through the radio. A packet may be formed by one or more chained frames.

In the file dash7/conf.h N_FRAMES is defined. N_FRAMES is a constant for the program that represents the maximum number of frames that can be contained in one packet. This variable is used to control the frames buffer that will be used by the PHY, so its value shouldn't be too large.

###### Data structure

###### phy_param_t
This structure contain the parameters that will be used to configure the transceiver for a procedure. This values are:
channel
preamble - if set to 0, the implementation will use the minimum number of bits specified by the draft
fec - set in case the used wants to use forward error correction, but no support is implemented here
pack_class - if the package will contain background of foreground frames
rssi_thresh - minimum value of noise in channel do collision avoidance methods
tx_eirp - the value here must be one of the gain options defined in sx1231.h

###### Functions

###### void phy_init()
This function must be called only once when the program star. It configures the transceiver with the values that cannot be changed within procedures.

###### void phy_proc_start()
Warn the PHY that a procedure is starting, so other procedures won't be executed together.

###### void phy_proc_finish()
Warn the PHY that a procedure has ended, so it can start attending other procedures.

All the other PHY functions must be called between phy_proc_start() and phy_proc_finish()

###### void phy_config(phy_param_t *conf)
Must be used right after phy_proc_start(). This function will configure the transceiver to use the parameters specified.

###### int phy_add_frame(uint8_t *frame)
this function receives a frame and put it in the buffer so they can be sended then phy_send_packet() is called. Since the procedure must be configured by this point, the PHY knows how to handle the frame size.
If the procedure is configured as a background frame procedure, it will assume that the frame has a fix size. IF it is configured as foreground frame, it will assume that the first byte from the frame will be the size of the frame (including the own size itself). The size of the frame must not include the CRC size, since this will be done by the PHY.
Once the frame is received, this function calculate its CRC value, update the size byte (frame length + CRC) and put it in the frame buffer.
IMPORTANT: If this function is called multiple times in a row, it will add more frames to be sended in the same packet, but if an other PHY function is called in between, the buffer is emptied.
This function return the amount of frames left empty in the buffer or a value smaller than 0 as an error.

###### int phy_send_packet(d7_ti ti, uint8_t ca)
Send a packet with the frames in the buffer. This function is also responsible for doing the pn9 (or data whitening) of the frames before sending them.
ti is the time that will be waited until the channel is clear to send.
ca is set when the user wishes to use collision avoidance mechanism.
Return 0 if ok, or a value smaller than 0 as error.

###### int phy_receive_packet(d7_ti ti)
ti is the time that this function will listen for a packet. This function will receive the packet, do its pn9 and place it in the buffer.
IMPORTANT: frames in the buffer always came from the same packet. If phy_receive_packet is called twice it will erase the frames that were received from the first one.

###### int phy_get_frame(uint8_t *frame, int max_size)
This function will take a frame from the buffer that was received by phy_receive_packet, will check for its CRC and will copy it to frame (without the crc and with the size of the frame in the first byte).
This function returns the number of frames that are still in the buffer.
Like phy_add_frame(), if another function from the PHY is called between two phy_get_frame(), the buffer is cleared.

###### phy_packet_rssi()
Return the rssi read by the transceiver when receiving the last packet. The value is the same returned by the transceiver, so the real value is -phy_pack_rssi()/2 dBm

###### Examples
In test/phy_test/ a code with examples of how dash7/phy.h should be used. In this example you can either set the program to send or receive a background or foreground frame.

###### dash7/data.h

This is the header of the data layer (DATA) implementation. The data layer will encapsulate most of the functions from the PHY and will now deal with all the parameters that are designed for it in the spec.

###### Data structure

###### data_param_t
These are the parameters that will be common to all procedures for the data layer. They must be setted in the global variable data_conf.
CSMAen - Set when the procedure will use CSMA mechanisms. (In this implementation it is the user responsibility to set this variable, it is not automatically assumed that CSMA will be used once a channel that enforce CSMA is chosen)
Ecca - Minimum noise in channel in order to do the CSMA mechanisms. This value works as the transceiver value, so the real value will be -Ecca/2 dBm
Tbsd - Duration of background scan.
Tca - Maximum time for CSMA mechanisms (if it is the CSMA takes longer, the packet won't be sent)
Tfsd - Duration of a foreground scan
Tg - Channel guard time (explained at data_guard_break())
Tl - Listen time after contention periode.

###### data_proc_param_t
Parameters that will be used in a DATA procedure
channel
pack_class
tx_eirp
fec
my_subnet - This is the only parameter that is now passed down to the PHY procedure. The subnet is used to filter incoming packets.

###### Functions

The DATA offers functions to configure the user address, but here will be only described the ones that will be used in procedures.

###### void data_proc_start()
This function starts a DATA procedure. It calls phy_proc_start(), so no need to start a PHY procedure within a DATA.

###### void data_proc_finish()
same as above

###### int data_add_frame()
same as above

###### int data_get_frame()
same as above

###### void data_proc_config()
same as above, but also deals with some parameters that remains in the DATA layer.

###### int data_guard_break(d7_ti time)
DASH7 specifies a guard time before sending packages (draft p27), this function tries to (within the timeout) wait until it's sure that the channel is not guarded anymore.
This function should not be used directly, it was made to be used within data_send_packet().

###### int data_csma(d7_ti time)
Add an extra random time before start sending a packet in a channel, this is also only used within data_send_packet().

###### int data_send_packet()
Send the frames that were passed to DATA or PHY. This functions calls phy_send_packet(), but before it does it, it respect the channel guarding and the csma

###### int data_send_packet_protected()
This is a macro to phy_send_packet(). This function must be called when the user is sure that the channel is already guarded for him, so there is no need to try to do CSMA or break a channel guard.

###### int data_listen()
Uses phy_receive_packet(). The difference is that no timeout is specified directly since they are configured by Tbsd and Tfsd. It will also handle background and foreground frame as specified by the specification (the Tbsd only starts if in the moment the scan starts the channel was already over the rssi limit).
###### int data_dialogue(systime_t sended, d7_ti Tc)
This function must only be called after a X_send_packet(). If the user expect an answer to the packet it sended, he/she must call this function after having send its packet but still within the procedure. What this function does is wait for the appropriate time (specified by ti) to pass after the time when the packet was sended in order to minimize the listening time. After Tc has passed, the procedure will listen during Tl (from data_conf global variable).
IMPORTANT: It is still up to the user to set the flag from the foreground frame that will specify the receiver that it must answer the frame, this is not done automatically.

###### int data_answer_time(systime_t received, d7_ti tc)
This function is used when there is the need to answer a packet. Once the packet is received and the answer is ready, this function is called so that that answer will be synchronized with the moment when it is expected. So this function comes after a data_listen or a phy_receive_packet and is immediately followed by a X_send_packet.

###### Examples
In tests/data_test/ source code can be found that will properly call for the new procedure functions.

###### dash7/bg_frames.h
This file offers functions to handle the background frame protocols. Even though it offers functions to directly control the frames, they should not be used, since there are others that will take care of them completely.

###### Data structure

###### bg_param_t
Here are all the parameters needed for a background frame
protocol
channel
time

###### Functions
Here only the functions that handle the background frame protocols are explained.

###### int advp_scan()
Try to listen for a background frame from the advertising protocol. If found, it will wait the time specified in the frame to then listen for the foreground frame in the channel that is also specified by the frame. If success is returned, the used can use data_get_frame() to read the foreground frame that was received. The packet may need an answer, so data_answer_time() may be needed before sending it.

###### int advp_send(uint8_t *frame, d7_ti time, uint8_t bg_channel, uint8_t fg_channel)
Advertise during 'time' at the bg_channel and then sends the frame through the fg_channel.
Since this function ends by sending a foreground frame, the user may as well use data_dialog() after it to check for an answer.

###### dash7/fg_frame.h
This file doesn't have any functions that handle directly with the radio, all functions are only used to edit the foreground frames before sending them to the other layers, so they won't be commented here.

###### Future Work
Some point in were ignored during this implementation. The FEC (forward error correction) and the DSSL for the foreground frames. They might need to be done, before continuing to implement the other layers.